CONFIDENTIAL

A921B

User Connectivity to the new JSE

Derivatives Trading

System

Version 2.6

March 2008

Produced by:	JSE Operations and Services

Reviewed by:	JSE Operations and Services

Version:	Version 2.5

Date:		June 2008

This document is confidential and contains property belonging to the JSE Limited (the JSE).  Neither this document nor its contents may be disclosed to a third party, nor may it be copied, without the JSE’s prior written consent.

CONFIDENTIAL

The JSE endeavours to ensure that the data and other material in this document are correct and complete but does not accept any liability for error herein or omission here from.  The development of JSE products and services is continuous and published information may not be up to date.  It is important that you check the current position with the JSE before acting on any information in this document.

| TABLE OF CONTENTS |  |
| --- | --- |

1.	References	6

2.	Version Control	7

3.    Introduction	7

4.    Glossary of terms	8

5.     User Connectivity	8

5.1 Connectivity to the JSE Network	8

5.2 Configuring Router for IP	10

5.3 Illustrations	10

5.4 Firewall / Router Configuration	15

5.5 Routing	16

5.6 Bandwidth Requirements	16

5.7 Client workstation minimum requirements	18

5.8 New front end availability	19

5.9 Information Subscriber requirements for the new Derivatives Trading System	19

6.     Contact List for Help or queries	20

# References

| Document* | Author | Version | Issue Date |
| --- | --- | --- | --- |

# Version Control

| Version | Author | Date | Reason for Changes |
| --- | --- | --- | --- |
| Version 2.0 | Matthias Kempgen | 12 February 2007 | Bandwidth requirements, Front End section, IP addreses |
| Version 2.1 | Matthias Kempgen | 13 February 2007 | Added NAS request process |
| Version 2.2 | Matthias Kempgen | 13 February 2007 | Glossary updated |
| Version 2.3 | Matthias Kempgen | 01 August 2007 | Added Production IP addresses and port numbers |
| Version 2.4 | Matthias Kempgen | 16 October 2007 | Added Windows VISTA as a supported Operating System |
| Version 2.5 | Matthias Kempgen | 01 March 2008 | Updated Bandwidth requirements and PC specifications Added backup link note under ‘Connectivity to the JSE network |
| Version 2.6 | Matthias Kempgen | 11 June 2008 | Link to download MSXML4 |

3. Introduction

The purpose of this document is to illustrate the connectivity options available to customers (Trading Members, Clearing Members and Information Subscribers) who will access the new JSE Derivatives Trading System for Agricultural Derivatives and Equity Derivatives.

The document caters for the acceptance and compliance test phases for the Derivatives System replacement and the production system addresses. The JSE reserves the right to change IP addresses and port numbers of the new Derivatives Trading System but will communicate any such changes.

Information Subscribers – please refer specifically to section 5.9 for information on infrastructure requirements for connection to the new systems via the API as well as all other sections of the document

# 4.  Glossary of terms

| IP | Internet Protocol |
| --- | --- |
| IPX | Novell Netware protocol (Internetwork Packet Exchange) |
| ISDN | Integrated Services Digital Network |
| JSE | JSE Ltd |
| NUTRON | NU TRading ONline |
| TCP | Transmission Control Protocol |
| Users | Recipients of JSE derivatives trading and information services |
| NAS | Network Access Service |

# 5. User Connectivity

## 5.1 Connectivity to the JSE Network

Currently members connect to the SAFEX system using dial-up, ISDN or leased lines, with routers configured for IPX.

To access the new system various options are available:

- Members can connect via existing leased lines currently being used for the production SAFEX systems. Members need to consider bandwidth utilisation on these circuits and impact to their current trading activities, and may as a result need to consider bandwidth upgrades to existing circuits. Routers must be configured for IP (see section 3.2 below).

- Members can elect to install new leased lines to facilitate connectivity to the new trading system.

- MTN Managed Network option – this option will enable users to connect to the JSE via the MTN MPLS network offering cost advantages and introducing connectivity options like leased line connectivity to a local MTN POP.

- ISDN dialup to the new Derivatives Trading System external user test environment and production environments is also available

Additional requirements for connectivity to the new trading system are:

- Private (as allocated by the JSE) class IP address space or public class IP address space

- Cisco router (recommended)

- In light of the soon to be released connectivity requirements market participants are reminded that a backup link to the JSE will become a mandatory requirement.

If the member chooses to use their own public class IP address space this needs to be communicated to the JSE via the Derivative_Info@jse.co.za e-mail address.

## 5.2 Configuring Router for IP

The member’s network and interface cards need to be enabled for TCP / IP connectivity. Sample router and switch configurations for TCP / IP networks can be obtained from www.cisco.com or member’s can contact their IT support provider.

For the JSE to configure members on TCP / IP, information is required and should be submitted to nas@jse.co.za as a NAS request for configuration. Please use the NAS template to complete your NAS request.

Should a member wish to connect via the MTN managed network solution members will be assisted with the setup.

## 5.3 Illustrations

The following three schematic diagrams outline the existing SAFEX connectivity as well as the proposed parallel new derivatives trading system and SAFEX test approach connectivity via a direct connection to the JSE or connectivity via the MTN managed network option.

Figure 1.  Existing Connectivity to SAFEX System

Figure 2. Connectivity to the new Derivatives Trading System during the Testing phase – SAFEX production system still in operation

Figure 3. Connectivity to the new Derivatives Trading System via the MTN Managed Network during the Testing phase – SAFEX production system still in operation

## 5.4 Firewall / Router Configuration

The following information is required to update firewall/router configurations if installed:

Test environment

- New Derivatives Trading System:

Proxy host address:	 	10.3.13.191

TCP port (Financials):		2003

TCP port (Agriculturals)		2210

- Download Server for updates:

Download Server host address:  			10.3.13.191

TCP port (downloads Financials and Agriculturals):	4410

Production environment

- Production Financials and Agricultural Trading Systems:

Proxy host address: 		10.3.5.131

TCP port (Financials): 		2003

TCP port (Agriculturals): 	2210

- Download Server for updates:

Download Server host address: 				10.3.5.131

TCP port (Financials and Agriculturals):			4410

## 5.5 Routing

Customers must use static routing to route data across the interface between the Customer Network and the JSE Network.

The following IP network configurations are required on the routers to facilitate connectivity to the test system:

Test environment:

IP route 10.3.13.191  255.255.255.255 (serial interface of router at the JSE)

Production environment:

IP route 10.3.5.131  255.255.255.255 (serial interface of router at the JSE)

## 5.6 Bandwidth Requirements

- Bandwidth Requirements for the new Derivatives Trading System Front End:

  - APD – 25k on average per user during a trading day (based on current production activity                          and will vary depending on the number of users per participating customer)

- Customers are requested to cater for the possibility of temporary spikes due to increased market activity

  - EDM – 25k on average per user during a trading day (based on current production activity                          and will vary depending on the number of users per participating customer)

    - Users can configure their front end to only ‘listen’ for updates on the instruments they are interested in viewing.

    - Please note that users need to cater for sufficient bandwidth in addition to this if they wish to use any algorithmic or autoquoting software/functionality (including the JSE’s own autoquote engine). This will also apply to users who wish to view all active instruments with autoquoting activity.

    - In addition JSE autoquote enabled users are able to view the underlying prices for all autoquote enabled instruments – this functionality requires at least 10k per user depending on the number of linked instruments

    - Customers are requested to cater for the possibility of temporary spikes due to increased market activity

- Bandwidth Requirements for Information Subscribers:

  - The JSE recommends 64k per ‘listener’ per market when listening to all instruments available.

- EOD file downloads:

- Specifications on these files are being finalised, however the JSE estimates that the complete set of available files will not exceed 2MB per day per market if all files are subscribed to.

## 5.7 Client workstation minimum requirements

The Derivatives Trading System front end application should be installed on a PC with the following recommended specifications (it is possible to install the new front end on the same workstation as your current SAFEX solution but is not recommended as this may impact your production trading activities):

Recommended:

P4 2.8 GHz or equivalent processor

512 MB RAM

Windows XP sp2

Minimum 2GB available disk space

Network Interface Card

OR

P4 2.8 GHz or equivalent processor

1024 MB RAM

Windows VISTA

Minimum 2GB available disk space

Network Interface Card

PLEASE NOTE:  The file downloads to HTML and XML from the front end require the MSXML4 pack to be installed on the workstation. This can be downloaded from:

http://www.microsoft.com/downloads/details.aspx?familyid=3144b72b-b4f2-46da-b4b6-c5d7485f2b42&displaylang=en

Users are advised that these base requirements do not cater for the trading front end in combination with other applications  (e.g. e- mail, pricing tools, etcetera). Each user is required to do sufficient testing to ensure their respective workstations are up to specification as required.

The JSE therefore recommends separating the physical installation of the new Derivatives Front End onto a separate PC or limiting their testing to times when the current ATS production front end is not used.

## 5.8 New front end availability

The new Derivatives Trading front end will be available for download from the JSE after 2 April 2007.

The JSE will communicate the link for the download of the software – the JSE will make the front end available via an FTP site and via the existing SAFEX Slaves.

## 5.9 Information Subscriber requirements for the new Derivatives Trading System

Information Subscribers will make use of the same API as the trading members– the API document for the new Derivatives Trading System (which is available separately) specifically indicates messages to be used by Information Subscribers to connect and access public information.

The current data feed servers (known as Newcoms) and related Digiboard infrastructure will no longer be valid and available once the new system goes live. Information Subscribers will require a leased line into the JSE to connect to the new system. The bandwidth requirements for information subscribers can be found in section 5.6. The sharing of existing Infowiz lines to the JSE will be possible as long as the shared line caters for all the bandwidth requirements as per section 5.6.

Please note that the new Derivatives Trading System API is based on the TCP/IP communications protocol – please refer to the new Derivatives Trading System API Specification document for more information.

# 6. Contact List for help or queries

Software or Technical Queries:

The JSE Trading Division can be contacted via the following e-mail address:

Derivative_Info@jse.co.za